## Slide 1: Kestrel-2 Tallgrass Evaluation Summary
Prepared by: Victor Nwosu
Two week evaluation, Tallgrass Semiconductor, Penang
Customer decision expected end of September 2026

## Slide 2: Measured Results
Metric | Requirement | Measured | Incumbent
Site-to-site temperature spread | < 1.5 C | 0.6 C | 2.4 C
Throughput (UPH) | 8,000 | 7,850 | 6,400
Changeover, trained engineer | < 25 min (published) | 31 min | 45 min
Changeover, customer operator | not specified | 52 min | 58 min
Contactor life (insertions) | 500,000 | 250,000 qualified | 480,000
Notes: Throughput measured on the customer's own device, four sites, minus 40 C.

## Slide 3: Open Items
Contactor life: customer believes our plunge force overshoots
Committed to return force data within eight weeks (mid August)
Published changeover specification to be corrected to under 30 minutes
Membrane dryer cartridge missing from the preventive maintenance schedule
Notes: The changeover number on the datasheet was a target that became a published specification. Product owns the correction.